Novel surface and interface probes using photoelectron spectroscopy:

standing waves, hard x-rays, and time resolution at high pressure

Charles S. Fadley

Department of Physics, University of California Davis, Davis, CA 95616 USA; and

Materials Sciences Division, Lawrence Berkeley National Laboratory, Berkeley, CA 94720 USA

I will discuss three relatively new developments in photoemission: the use of nanometer-scale standing-wave (SW) excitation so as to selectively look at different depths below the surface [1-3], the use of harder x-ray excitation in the multi-keV range so as to probe more deeply below the surface, in what has been termed HAXPES or HXPS [4], and the use of differentially pumped sample cells to carry out measurements at elevated pressures in the multitorr regime [5].  The first two of these approaches have the potential for enhancing the sensitivity of photoemission to both bulk and buried interface properties, while at the same time permitting the study of near-surface phenomena.  The third permits bridging the “pressure gap” so as to study surface chemical reactions under more realistic conditions. After a brief overview of basic concepts, I will discuss several recent applications of these methods, separately and in concert.  These will include: variable-temperature HXPS measurements at the ESRF on fractured cubic and cleaved bilayer lanthanum strontium manganite samples [6,7], SW HXPS measurements at BESSY [8] and SPring8 [9] on systems of relevance to spintronic applications, the possibility of doing angle-resolved HXPS so as to carry out band mapping [10], the possible benefits of photoelectron diffraction in the hard x-ray regime for local structure determinations [11], and the application of high-pressure XPS to the oxidation of Si [5].

---------------------------------------------------------------------------------------------------------------------------------

This work was supported by the U.S. Department of Energy under Contract No. DE-AC02-05CH11231, the Helmholtz Association and the Humboldt Foundation.

[1]  "Probing Buried Interfaces with Soft X-ray Standing Wave Spectroscopy: Application to the Fe/Cr Interface", S.-H. Yang, B.S. Mun, N. Mannella, S.-K. Kim, J.B. Kortright, J. Underwood, F. Salmassi, E. Arenholz, A. Young, Z. Hussain, M.A. Van Hove, and C.S. Fadley, J. Phys. Cond. Matt. 14, L406 (2002).

[2] “Spectroscopic Characterization of Buried Interfaces Using Soft X-ray Standing Waves”, S.-H. Yang, B.S. Mun, and C.S. Fadley, Synchrotron Radiation News 17 (3), 24 (2004).

[3]  “Correlation of magnetic tunnel resistance and buried-layer densities of states from standing-wave soft x-ray photoemission”, S.-H. Yang, B. S. Mun, N. Mannella, A. Nambu, B.C. Sell, S. B. Ritchey, F. Salmassi, S. S. P. Parkin, C. S. Fadley, J. Phys.: Condens. Matter 18,  L259–L267 (2006).

[4] “X-Ray Photoelectron Spectroscopy and Diffraction in The Hard X-Ray Regime: Fundamental Considerations and Future Possibilities”, C. S. Fadley, Nuclear Instruments and Methods A 547, 24-41 (2005), other papers in this special journal issue edited by J. Zegenhagen and C. Kunz, and subsequent workshop summaries available at: http://haxpes2006.spring8.or.jp/program.html and http://ssg.als.lbl.gov/ssgdirectory/fedorov/workshops/index.html .

[5]  “Real-Time Observation of the Dry Oxidation of the Si(100) Surface with Ambient Pressure X-ray Photoelectron Spectroscopy” Y. Enta, B. S. Mun, Y. Enta, M. Rossi, P. N. Ross, Z. Hussain, C.S. Fadley, K.-S. Lee, and S.-K. Kim, Appl. Phys. Lett. 92, 012110 (2008).

[6]  “Bulk electronic properties of the bilayered manganite La1.2Sr1.8Mn2O7 from hard-x-ray photoemission“, F. Offi, P. Torelli, M. Sacchi, P. Lacovig, A. Fondacaro, G. Paolicelli, S. Huotari, G. Monaco, C.S. Fadley, J.F. Mitchell,  G. Stefani, and G. Panaccione, Phys. Rev. B 75, 014422 (2007).

[7]  “Temperature-Dependent Electronic Structure of the Colossal Magnetoresistive Manganite La0.7Sr0.3MnO3 via Hard X-Ray Photoemission”, F. Offi, N. Mannella, T. Pardini, G. Panaccione, A. Fondacaro, P. Torelli, S. Huotari, M. W. West,  J. W. Mitchell and C.S. Fadley, Phys. Rev. B 77, 174422 (2008).

[8]  F. Kronast, S. Döring, M. Gorgoi, R. Ovsyannikov, A. Kaiser, C. Wiemann, S.-H. Yang,

M. Huijben, A. Locatelli, D. E. Bürgler, R. Schreiber, F. Schäfers, W. Braun, H.A. Dűrr, C. M. Schneider, C. Westphal, C. S.  Fadley, Appl. Phys. Lett. 93, 243116 (2008)

[9]  C. Papp, B. Balke, S. Ueda, H. Yoshikawa, K. Kobayashi, D. E. Bürgler, R. Schreiber, C. M. Schneider, K. Jenkins, C. Felser, and R. Ramesh, to be published.

[10]  “Band Mapping in Higher-Energy X-Ray Photoemission: Phonon Effects and Comparison to One-Step Theory”, L. Plucinski, J. Minár, B.C. Sell, J. Braun, H. Ebert, C.M. Schneider and C.S. Fadley, Phys. Rev. B 78, 035108 (2008).

[11] A. Winkelman, C.S. Fadley, and J. Garcia de Abajo, New J. Phys. 10, 113002 (2008).